## Slide 1: Extensions + Colour Mapping
Laser Cutting:
Presented by Makerspace

## Slide 2: Do You Have a Makerepo Account?
Make an account on Makerepo.com so that you can have access to other people’s projects and the use of our space! Everyone NEEDS one.
Community members speak to those working in the makerspace to get setup!

## Slide 3: Inkscape Advanced Features
Colour Mapping
  Allows you to assign different values for specific colours in your design
    Speed
    Power
    Frequency
  Therefore no need to run separate jobs
  More depth in rastering jobs
Extensions
  Created by the community
  Allow you perform complex functions simply
    Laser cut box template
    Living hinges

## Slide 4: Why use Colour Mapping?
Allows for greater flexibility in your designs
More dynamic looking cuts
  Darker spots can be made by setting the power/frequency to a higher value
  Change vector power to change depth of cut
  Results will vary depending on the material

## Slide 5: Colour Mapping
In order to colour map your file you are going to first need to follow a few steps.
Step 1:
Create a design in Inkscape that uses different colours for vectoring/ rastering
It is important to use basic colours as they are easier to map (simple RGB)
Simplifies the process when we move over to the Epilog software

## Slide 6: Colour Mapping
Step 2:
Export your file as a PDF and load up Epilog’s software
  Ensure Colour Mapping is selected
  Set the colour based on RGB values (use 255 values ONLY)
  Set the Speed, Power, Frequency values for that colour
    Indicate if you are rastering/vectoring
  Navigate colour profiles using the Plus or Minus
*Note this software is only on the laptop connected to the laser cutter.

## Slide 7: Extensions?
Extensions that are created by the Inkscape Community and are used to make designing easier or to add more functionality
  They are simple to install and increase the capabilities of the software
https://inkscape.org/en/gallery/=extension/
Online database of a few extensions
Open source allowing you to make your own extensions
Extensions built into Inkscape can be accessed from the Extension toolbar:
  The function/use of these will vary
  Install files will indicate how these work

## Slide 8: Living Hinge Extension
What is a living hinge?
Series of relief cuts that allows a solid material to have bending properties
You can design much more complex shapes for various applications
Issues:
To preform cuts like this it is very time intensive to cut and design
  Using the extension it will design everything for you
Area becomes much weaker
https://inkscape.org/en/~drphonon/%E2%98%85living-hinge-creator

## Slide 9: How to install an Extension?
Steps to follow:
Download and unpack the archive file from the website
Determine the location of where to copy these files
  In Inkscape:
    Edit > Preferences > System: User Extensions
Locate this path on your computer
  Copy the two files from the download (.inx and .py files)
Restart Inkscape and you should now be able to access it from the Extensions on toolbar

## Slide 10: Living Hinge Extension
In order to access the Living Hinge extension we need to follow the path:
Extensions > Render > Living Hinge
Different extensions may be placed elsewhere, usually included in description of download
*Note you will also see some extensions already built into Inkscape
Since the Extensions are Community made the instructions on how to use them will be provided on the main page on which you downloaded them
The Living Hinge came with the following information page:
http://wiki.lvl1.org/Inkscape_Extension_to_Render_a_Living_Hinge

## Slide 11: Using the Living Hinge
Step 1: Create a Rectangle object that you wish to contain the living hinge within
Step 2: Access the Living Hinge Extension and select “Live Preview”, the appropriate lines should now be showing to make a living hinge

## Slide 12: Using the Living Hinge
Step 3: Within the Living Hinge extension we can change certain features about the hinges including
Step 4: Now we have a completed Object that will act as a living hinge once cut by the laser
Delete the original rectangle you’ve placed depending on your design
  *Ensure you change the stroke weight of the line back to 0.001 in. if you are Vectoring

## Slide 13: Additional Extensions
There are many extensions you can try out and install from Inkscape’s website
The installation process will be very similar
  ALWAYS read the description of the extension you wish to install
If you have additional questions feel free to ask the workshop manager
*Note: You can also download Living Hinge projects that have already been created from Thingiverse
Enjoy Making!!

## Slide 14: Try it Out! (Living Bracelet)
*Note:
Create a relatively small design as both functions are quite time consuming for the laser to perform.
Create a simple raster-able pendant that utilizes the colour mapping functionality
Now make the bracelet straps but setting a living hinge along those edges
Create holes for tying ends together
When creating the straps and connection point make sure the correct area are being vectored
  (Bezier Curve Tool is Ideal) + Avoid overlapping shapes

## Slide 15: Want to be a volunteer??
Go to volunteer.makerepo.com and get trained!
Here you can find the rewards for volunteer hours and some of the things you can do to get involved.
HOPE TO SEE YOU THERE!!

## Slide 16: PLEASE FILL OUT THIS SURVEY
Survey.makerepo.com
Help us improve our workshops, it only takes a minute.
We are open 12-8 Mondays to Friday and Sundays 11-5 (Community Hours)